## Slide 1: BRINGING TRITON TO AMD GPUs
Jason Furmanek, Lixun Zhang

## Slide 2: AMD GPU Backend Status update
Support began about one year ago
  Originally explored as dependency of DeepSpeed​
  Pytorch 2.0 accelerated our involvement
Where is the code?​
  Now enabled as a 3rd-party backend! https://github.com/openai/triton/pull/1983
  Links to a commit in our repository
    http://github.com/ROCmSoftwarePlatform/triton
  AMD GPU backend development continues here; submodule commit will be periodically updated
Hardware Support​
  Support CDNA GPUs (AMD Instinct MI100/MI200)​
  Experimental support on RDNA GPUs​
  Device detection at runtime
Full support for torch.compile in Pytorch 2.0
  Pytorch 2.1 support in progress
When calling into triton.compile, use device_type="hip"​

## Slide 3: Scoping the port
Why Triton (on AMD GPUs)?
  Support Deepspeed and pytorch
  Lots of customer interest
Triton design to block at the kernel level vs the thread level
  Designed on NVIDIA but also a natural fit for AMD GPUs
  All the good design of the Triton can also benefit AMD GPUs
LLVM and MLIR
  AMD ROCm toolchain is upstream LLVM based
  AMD has already invested heavily in LLVM and MLIR
Dialect needs
  TritonGPU IR mostly re-used
    no new ops added to TritonGPU Dialect
    Lower dotOp to MFMA layout added
Shared memory access to avoid shared memory bank conflicts
  same swizzling patterns
  Conserve LDS space in favor of VGPR usage (example: Keep Q tensors in registers)
Port PTX usage with amdgcn assembly and MLIR
MatrixCore (MFMA)
  Multiple layouts/sizes supported
Up to 220 CUs
(4) 16 lane SIMDs per CU
512 VGPRs
Shared Memory
  64k Local Data Store (LDS)
  32 banks
128 GB HBM2e
AMD INSTINCT MI200 (CDNA2)

## Slide 4: Triton Enablement Approach
Support Empty Kernel
Support base set of Triton Ops
Memory, math, creation, linearAlgebra, reduction
Dot via vector FMA
Enable Matrix Core support
dot
FlashAttention
Maximize Occupancy and Efficiency
Increased wavefronts per CU
Pipelining
Swizzling
Wavefront size
Kernel launcher
Softmax
“We” are here

## Slide 5: ROCM third party backend
The ROCm build now is a submodule
https://github.com/openai/triton/tree/main/third_party
  -> amd_hip_backend @ d0ad70d
  Currently links to a branch in github.com/ROCmSoftwarePlatform/triton
Built it! Checkout –recursive to grab all submodules
  export TRITON_CODEGEN_AMD_HIP_BACKEND=1
  git clone http://github.com/openai/triton --recursive
  cd triton/python
  pip install –e .
Changes for ROCm
  Move dialect changes to TritonGPUROCM Dialect
    Mlir::rocm::triton::gpu
    /lib/Dialect/TritonGPUROCM
  /lib/Conversion/TritonGPUROCMToLLVM is mostly a copy of TritonGPUToLLVM, but we're working to make it more precise

## Slide 6: Optimizations on AMD Instinct GPUs

## Slide 7: AMD Matrix Cores
Multiplicand A
Multiplicand B
Accumulators (C or D)
Support full range of mixed precision operations for GEMM
Matrix fused multiply add (mfma) instructions
  Format: mfma_CDfmt_MxNxKABfmt
  Performance: see table below
Layout of mfma_f32_32x32x8f16
  Layout: elements distribution among threads in a warp
  warpSize = 64
  Multiplicand B and Accumulator have the same layout
  Multiplicand A and Accumulator’s layouts are “transposed”
Data format | MI250X flops/Clock/CU
FP64 | 256
FP32 | 256
FP16 | 1024
BF16 | 1024
INT8 | 1024

## Slide 8: Chained dot
The result of first dot is served as input to the second dot
Which input?
  For input B, good to go
  For input A, naïve implement requires LDS to transpose the output layout
For flash attention forward kernel, result of first dot is used as input A of the second dot.
Multiplicand A
Multiplicand B
Accumulators (C or D)

## Slide 9: Chained dot --- optimization
SW: swaps operands
HW: interprets data “transposed”
Math:
mfma layout on = mfma.trans layout on
Now it’s ready to be used as multiplicand A for the next dot
Transposition is achieved without transposing anything

## Slide 10: Software pipelining
One buffer in LDS, more buffers in VGPRs
compute contains LDS_read and mfma
  It always starts with data in LDS
One or more compute and global_load are overlapped
Save LDS, but increase register pressure
2 stages  1 VGPR

## Slide 11: More optimizations
Keep Q in registers for small head_dim
Keep wavefronts vertically stacked, (i.e., warpsPerCTA={n, 1})
Reorder pointer arithmetic to maximize global load vector length
Tune waves-per-eu attribute
  It can limit the number of registers used by each wavefront, spilling can happen
  It can increase the number of wavefronts running concurrently

## Slide 12: Current Performance on AMD Instinct GPUs

## Slide 13: Performance with AMD Instinct MI250 --- GEMM
Dense GEMM for M=N=K=1024 ~ 8192
Larger gap with small GEMMs
We have more optimizations on the Todo list
  Store mfmaEncodingAttr directly to global memory without going to LDS
  Control wavefronts scheduling at finer granularity
Chart: Triton/rocBLAS
| 1024 | 2048 | 4096 | 8192
Series 1 | 0.62 | 0.88 | 0.81 | 0.9

## Slide 14: Performance with AMD Instinct MI250 --- Flash attention fwd
Standalone flash attention forward kernel performance (triton tutorial)
  Batchsize=4, nheads=48, head_dim=64
  dropout=0, causal=False
NVIDIA DGXA100
  CPU: 2xAMD EPYC 7742 64-core
  GPU: Nvidia A100 80GB SXM
MI250 Supermicro 4124
  CPU: AMD EPYC 7763 64-core
  GPU: AMD Instinct MI250 OAM (128 GB HBM2e)
More optimizations
  Software pipelining
  We expect improvement of GEMM helps FA performance
Chart: FA fwd bs4-h48-d64, dropout=0, causal=False
| 1024 | 2048 | 4096 | 8192 | 16384
Triton-MI250 | 160.8217 | 185.41 | 196.285 | 202.3733 | 206.1767
Triton-A100SXM | 137.964 | 184.246 | 193.566 | 196.132 | 197.366

## Slide 15: Questions?

## Slide 17: Backup slides

## Slide 18: Introduction to AMD GPUs
Two AMD GPU Families
  AMD Instinct (CNDA): Target Data Centers
  AMD Radeon (RDNA): Target Workstations and Gaming
Some key differences relevant to Triton
  CDNA 2 (MI250): 64 threads per Wavefront, MatrixCore (MFMA), FP16/BF16/INT8/INT4, OAM/PCIe, Infinity Fabric, 128G HBM2, 64k LDS
  RDNA 3 (Navi): 32 threads per Wavefront, Wave MMA (WMMA), FP16/BF16/INT8/INT4, PCIe, 12G GDDR6
Architecture Capability Set defined in a "gfx" arch
  CNDA 2: gfx9xx (i.e., gfx90a == MI200)
  RDNA 3: gfx11xx
Software Stack
  Triton Dialect (ttir, ttgir)
  LLVM
  Amdgcn (assembly), hsaco
  ROCm Runtime
Terminology
  Warp => wavefront (64)
  ThreadBlock => workGroup (up to 16)
  Thread => workitem
  MMA => MFMA

## Slide 19: Our progress on Flash attention fwd kernel
optimizations | speedup
Keep qk/p in register, a.k.a. the optimization for chained dot | 
Disable swizzling computation | 52%
Keep q in register | 13%
Enable swizzling for k-major matrices | 15%
Maximize global_load vector length via block_ptr semantics* | 26%
Set qk type to float32 | 9%
Set waves-per-eu=3 | 24%
* Note: we saw 150% perf improvement after maximizing global_load vector length for GEMM